Exporter –

Installing

Left < > Right Swap Patch 4.2.0p2

IS09013

Issue 0.1	07 August, 2009

IS09013 Exporter – Installing Left < > Right Swap Patch

INFORMATION SHEET

1  INTRODUCTION

iBiquity IRSS 4.2.0p1 was released with a bug that caused the left/right audio channels to be reversed. Subsequently a patch was released which corrects this problem. This document describes how to install this Left < > Right swap patch.

NOTE

This patch is considered an interim solution. The system will display some warnings. During bootup, a “Verification Fail” will be displayed in red text. Also, the version (4.2.0p2) will be displayed in red as shown in Figure 1.

These warnings will not affect the performance of the system.

## 2  INSTALLING CD

For Exporters configured with Nautel Release 4.0 (iBiquity IRSS 4.2.0p1) install the Left < > Right swap patch as follows:

- Turn on the Exporter and insert the Left < > Right swap patch CD into the Exporter’s CD drive.

- See Figure 1. Select Command from the SYSTEM dialog.

- See Figure 2. From the System Command dialog box, enter the text “installcd” in the Command field. Select the “Display Results” check box and click the Execute button.

- Successful installation will be displayed as shown in Figure 3.

- Restart the Exporter.

Figure 1: SYSTEM – Command selection

Figure 2: System Command menu - Install CD

Figure 3: Successful installation display

# Text boxes

# Nautel Limited

10089 Peggy's Cove Road,

Hackett's Cove, NS, Canada B3Z 3J4

T.877 6 nautel (628835) or +1.902.823.2233
F.+1.902.823.3183 info@nautel.com

U.S. customers please contact:

Nautel Inc.

201 Target Industrial Circle, Bangor ME 04401

T.877 6 nautel (628835) or +1.207.947.8200

F.+1.207.947.3693  info@nautel.com

e-mail: support@nautel.com

www.nautel.com

( Copyright 2009 NAUTEL. All rights reserved.

red text