## Slide 1: SNMP Putting the Simple back in Simple Network Management Protocol

## Slide 2: What is it?
SNMP was developed in 1988
  Purpose is to collect and organize data from devices on a network
  Can also send information to manage devices and change behaviour
  Provides an easy way to monitor and control anything that is connected

## Slide 3: What is the structure?
Manager
(MIBs)
Agent
(MIB1)
Agent
(MIB2)
Agent
(MIB3)
Agent
(MIB4)
Device 1
Device 3
Device 2
Device 4

## Slide 4: What is the structure?
Managers – poll the agents to retrieve status, or push (SET) commands
Agents/Clients – retrieve information from the devices to send to managers, or take commands from managers and send to devices
Browsers – a visual tool to view the overall activity, to monitor status for each device, or to provide a simple way to send commands to the devices.

## Slide 5: What is the structure?
MIBs
Management Information Base
Everything there is to know in too many numbers!

## Slide 6: What is the structure?
MIB files
  Management Information Base
    Predefined structure that stores information that can be queried or set
    Work from a very structured address set (OID – or Object Identifier)

## Slide 7: What is the structure?
OID: .1.3.6.1.4.1.28142.1.300.256.329.0
  1.3.6.1 = iso.org.dod.internet (this will be the same for all devices)
  4 = private (1 – directory, 2 – management, 3 – experimental, 5 – security, 6 – SNMPv2, 7 – mail, 8 - features
  1 = enterprise
  28142 = manufacturer code (Nautel is 28142)
  1 =
  300 = product identifier (in this case, VS300 transmitter)
  256 =
  329 =
  0 =

## Slide 8: What are the commands?
Get
Get Response
Get Next
Walk
Set
Trap
Inform

## Slide 9: How do we make it work?
Configure devices
  Set Community PWs
  Enable Traps
  Set IP of Manager for receiving Traps

## Slide 10: How do we make it work?
Configure devices
  For Traps, select what alarms or functions will send notifications to Manager.

## Slide 11: How do we make it work?
Configure Manager
  Set Server (Agent) IP address and login info.
  Note that some managers will require a password (leaving blank may not be an option!)

## Slide 12: How do we make it work?
Configure Manager
  Import (load) MIBs for all client devices

## Slide 13: How do we make it work?
Configure Manager
  Nautel provides MIBs in FTP site
http://www3.nautel.com/pub/SNMP_MIBs/

## Slide 14: How do we make it work?
There are several IT related managers/browsers
  iReasoning
  Loriot
  PRTG
  Zabbex
  Etc.

## Slide 15: How do we make it work?
Can import MIB
Select what to watch
Or manually enter
Use MIB for reference

## Slide 16: How do we make it work?
Reporting can be as simple (or complex) as you make it

## Slide 17: The Gotchas
There are always gotchas. 
  SNMP requires ports 161 and 162 be open (161 for messages from the manager to the agent, 162 for messages going the other way).
  Different managers will require different amounts of configuration
    A simple MIB browser needs very little config – but offers little organization
    A more complex manager can be configured all the way to putting analog meters up.

## Slide 18: Questions?

## Slide 19: Online Information
Webinars https://www.nautel.com/resources/webinars/
YouTube http://www.youtube.com/user/NautelLtd
Nautel Waves Newsletter https://www.nautel.com/newsletters/

## Slide 20: Nautel Major Product Families
XR and NX Series AM transmitters
NX25
3.5kW – 88kW
300W – 2.5kW
GVSeries FM
VSSeries FM
3kW – 2.0MW
Advanced User Interface (AUI)
NX200
NX300
NX400
NX100
NX50
NVLTSeries FM
3.5kW – 10kW
Now all Nautel transmitters are shipped with a
FOUR YEAR WARRANTY!
XR3
XR6
XR12
Notes: The numbers next to the transmitters indicate wattage, so XR3 = 3000 watts
On NavAids it is different, typically it is 4x power

## Slide 21
Thank You